## Slide 1: CS 203 Project Air Pollution Monitoring System
Group Members:
Aminesh Kumar Rai 2018314
Aryan Singh 2018320
Prakash Prajapat 2018350

## Slide 2: About the project: We are using some simple and cost effective material to make to make a simple air quality monitoring system. We will monitor the air quality present in our surrounding and will trigger the alarm as the air quality goes down beyond a certain level.

## Slide 3: Working Principle: When we place our device near a place where there are harmful gases like CO2, NO2, the red LED will glow and the buzzer will start ringing. If there is a good quality air near it, then the green LED will glow.

## Slide 4: Materials Required
Seeed Grove-Gas Sensor (MQ2)
Arduino Uno
Buzzer
Breadboard
Resistor (221 ohm)
Red Green LED

## Slide 5: Procedure
Arduino's digital 10 pin is connected with buzzer.
Digital 9 pin and Digital 8 pin connected with LED green and LED red respectively with 100 ohm resistor.
Buzzer and Both LEDs are grounded.
Analog A0 is connected with gas-sensor's OUT and VCC connected with 5V and GND is grounded.

## Slide 6: Code: For Gas Detector (1/2) int redLed = 12; int greenLed = 8; int buzzer = 10; int smokeA0 = A0; // Your threshold value int sensorThres = 150; void setup() { pinMode(redLed, OUTPUT); pinMode(greenLed, OUTPUT); pinMode(buzzer, OUTPUT); pinMode(smokeA0, INPUT); Serial.begin(9600); } void loop() { int analogSensor = analogRead(smokeA0); Serial.print("Pin A0: "); Serial.println(analogSensor);

## Slide 7: Code: For Gas Detector (2/2) // Checks if it has reached the threshold value if (analogSensor > sensorThres) { digitalWrite(redLed, HIGH); digitalWrite(greenLed, LOW); tone(buzzer, 3000, 300); } else { digitalWrite(redLed, LOW); digitalWrite(greenLed, HIGH); noTone(buzzer); } delay(100); }

## Slide 8
Circuit Diagram with Green LED ON

## Slide 9
Circuit Diagram with
Red LED ON

## Slide 10: Conclusion
The air pollution detector works fine giving a red signal and a buzzer alarm when subjected to high air pollution environment and green signal with no alarm when subjected to air pollution level below threshold.

## Slide 11: THANK YOU